## Slide 1: RIP

## Slide 2: Approaches to Shortest Path Routing
There are two basic routing algorithms found on the Internet.
1. Distance Vector Routing
Each node knows the distance (=cost) to its directly connected neighbors
A node sends periodically a list of routing updates to its neighbors.
If all nodes update their distances, the routing tables eventually converge
New nodes advertise themselves to their neighbors
2. Link State Routing
Each node knows the distance to its neighbors
The distance information (=link state) is broadcast to all nodes in the network
Each node calculates the routing tables independently

## Slide 3: Characteristics of Distance Vector Routing
Periodic Updates: Updates to the routing tables are sent at the end of a certain time period. A typical value is 90 seconds.
Triggered Updates: If a metric changes on a link, a router immediately sends out an update without waiting for the end of the update period.
Full Routing Table Update: Most distance vector routing protocol send their neighbors the entire routing table (not only entries which change).
Route invalidation timers: Routing table entries are invalid if they are not refreshed.

## Slide 4: RIP - Routing Information Protocol
A simple intradomain protocol
Straightforward implementation of Distance Vector Routing
Each router advertises its distance vector every 30 seconds (or whenever its routing table changes) to all of its neighbors
RIP always uses 1 as link metric
Maximum hop count is 15, with “16” equal to “”
Routes are timeout (set to 16) after 3 minutes if they are not updated

## Slide 5: RIP Messages
This is the operation of RIP in routed. Dedicated port for RIP is UDP port 520.
Two types of messages:
  Request messages
    used to ask neighboring nodes for an update
  Response messages
    contains an update

## Slide 6: Routing with RIP
Initialization: Send a request packet (command = 1, address family=0..0) on all interfaces:
    RIPv1 uses broadcast if possible,
    RIPv2 uses multicast address 224.0.0.9, if possible
requesting routing tables from neighboring routers
Request received: Routers that receive above request send their entire routing table
Response received: Update the routing table
Typically, there is a routing daemon (routed) that is an application layer process that provides access to routing tables.

## Slide 7: Routing with Rip Cont.
Regular routing updates: Every 30 seconds, send all or part of the routing tables to every neighbor in an response message
Triggered Updates: Whenever the metric for a route change, send entire routing table.
If a router does not hear from its neighbor once every 180 seconds, the neighbor is deemed unreachable.

## Slide 8: RIP Problems
RIP takes a long time to stabilize
  Even for a small network, it takes several minutes until the routing tables have settled after a change
RIP has all the problems of distance vector algorithms,
The maximum path in RIP is 15 hops

## Slide 9: An Example of RIP
Routers advertise the cost of reaching networks.
In this example, C’s update to A would indicate that C can reach Networks 2 and 3 with cost 0, Networks 5 and 6 with cost 1 and Network 4 with cost 2.

## Slide 10: RIP TIMERS
The routing information protocol uses the following timers as part of its operation:[
Update Timer: controls the interval between two Response Messages. By default the value is 30 seconds. The response message is broadcast to all its RIP enabled interface.
Invalid Timer: The invalid timer specifies how long a routing entry can be in the routing table without being updated. This is also called as expiration Timer. By default, the value is 180 seconds. After the timer expires the hop count of the routing entry will be set to 16, marking the destination as unreachable.[19]
Flush Timer: The flush timer controls the time between the route is invalidated or marked as unreachable and removal of entry from the routing table. By default the value is 240 seconds. This is 60 seconds longer than Invalid timer. So for 60 seconds the router will be advertising about this unreachable route to all its neighbours. This timer must be set to a higher value than the invalid timer.[19]
Holddown Timer: The hold-down timer is started per route entry, when the hop count is changing from lower value to higher value. This allows the route to get stabilized. During this time no update can be done to that routing entry.. The default value of this timer is 180 seconds.[19]